Distributed Online Call Control on General Networks

---------------------------------------------------

The internet is increasingly used to transmit data of real-time

applications such as audio and video. Thus, the provisioning of

Quality-of-Service over the internet is becoming of key importance.

In this work we consider the problem of the online admission and

routing of connection requests, each one requesting the reservation of

end-to-end bandwidth between the communicating parties. This problem

is many times referred to as the "call control problem". We give novel

online randomized algorithms on general network topologies, that with

high probability achieve at least a polylogarithmic fraction of the

optimal solution.

The decisions of our new algorithms do not depend on the current load

of {\em all} network links, as in previous algorithms for general

network topologies (the Awerbuch, Azar, Plotkin algorithm of 1993). Instead,

their admission decisions depend only on link loads along a single path

between the communicating parties. They can thus be performed in a

distributed hop-by-hop manner through the network. Furthermore, our

algorithms can handle concurrent requests in the network. These

properties make our algorithms applicable in the framework of

existing internet protocols.

Joint work with Harald Raecke.